## Slide 1
Digital Logic & Design
Lecture 02
Notes: 1

## Slide 2: Number Systems and Codes
Decimal Number System
Octal Number System
Hexadecimal Number System
Caveman Number System
Binary Number System
Notes: 2
Let us start our discussion with Number Systems.
Earlier we have discussed that Digital Systems can process different types of information such as numbers, text, pictures and sound which are represented in the form of Binary numbers.
For understanding the Digital System we need to be fully aware of the Binary Number System and should be able to perform all the functions and operations that we have been performing using the Decimal Number System.
We would be looking at five different Number Systems.
We will start our discussion with the Decimal Number system. We are already aware of the Decimal number system and have been using the decimal number system since our school days.
Next we would be discussing a hypothetical Caveman Number System. I am using the Caveman number system as an example to introduce a Number system which is different from the decimal number system.
The third Number System that I would be discussing is the Binary Number System used by digital systems
The last two number systems that I would be mentioning are the Hexadecimal and the Octal Number systems.

## Slide 3: Decimal Number System
Ten unique numbers 0,1,2,3,4,5,6,7,8,9
Combination of digits
Positional Number System
275 = 2 x 102 + 7 x 101 + 5 x 100
  Base or Radix 10
  Weight 1, 10, 100, 1000 ….
Notes: 3
The decimal number system has ten unique digits 0, 1, 2, 3… 9
Using these single digits, ten different values can be represented
To represent values greater than ten, the digits have to be used in different combinations. Thus ten is represented by the number 10, two hundred seventy five is represented by 275 etc. Thus same set of numbers 0,1 2… 9 are repeated in a certain order.
The decimal number system is a positional number system as the position of a digit represents its true magnitude. For example 2 is less than 7, however 2 in 275 represents 200, whereas 7 represents 70. The left most digit has the highest weight and the right most digit has the lowest weight.
The weight of subsequent digits increases by a factor of 10 towards the left starting with 1 as the weight of the right most digit or the least significant digit.
275 can be written as 2 x 102 + 7 x 101 + 5 x 100 = 200 + 70 + 5 = 275
  The 10 represents the base or radix
  102, 101, 100 represent the weights 100, 10 and 1 of the numbers 2, 7 and 5

## Slide 4: Representing Fractions
Fractions can be represented in decimal number system in a manner
= 382.91
= 300 + 80 + 2 + 0.9 + 0.01
= 3 x 100 + 8 x 10 + 2 x 1 + 9/10+ 1/100
= 3 x 102 + 8 x 101 + 2 x 100 + 9 x 10-1+ 1 x 10-2
Notes: 4
Fractions can be represented in decimal number system in a manner similar to that of representing integers.
The weight of the digit to the immediate right of the decimal point has a weight 10-1.
Weights of subsequent digits decreases by a factor of 10.
Thus 382.91 can be written in terms of the base number and weights as
3 x 102 + 8 x 101 + 2 x 100 + 9 x 10-1 + 1 x 10-2
Solving the expression results in five terms 300, 80, 2, 0.9 and 0.01 which sum up to 382.91

## Slide 5: Octal Number System
Base 8
0, 1, 2, 3, 4, 5, 6, 7
Representing Binary in compact form
  11011000001102 = ?

## Slide 6: Octal Number System
Base 8
0, 1, 2, 3, 4, 5, 6, 7
Representing Binary in compact form
  11011000001102 = 154068

## Slide 7: Counting in Octal
Decimal | Binary | Octal
0 | 000 | 0
1 | 001 | 1
2 | 010 | 2
3 | 011 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7

## Slide 8: Counting in Octal
Decimal | Octal | Decimal | Octal | Decimal | Octal
8 | 10 | 16 | 20 | 24 | 30
9 | 11 | 17 | 21 | 25 | 31
10 | 12 | 18 | 22 | 26 | 32
11 | 13 | 19 | 23 | 27 | 33
12 | 14 | 20 | 24 | 28 | 34
13 | 15 | 21 | 25 | 29 | 35
14 | 16 | 22 | 26 | 30 | 36
15 | 17 | 23 | 27 | 31 | 37

## Slide 9: Octal Number To Decimal Number Conversion
( 26 ) 8 = ( ? ) 10
= (2 x 81) + (6 x 80)
= 2x8 + 6x 1
=16+ 6= (22)10

## Slide 10: Octal Number To Decimal Number Conversion
( 4033) 8 = ( ? ) 10

## Slide 11: Octal Number To Decimal Conversion
( 4033) 8 = ( ? ) 10
=(4 x 83) + (0 x 82) + (3 x 81) + (3 x 80)
=(4 x 512) + (0 x 64) + (3 x 8) + (3 x 1)
=2048 + 0 + 24 + 3 = (2075)10

## Slide 12: Octal FRACTIONS To Decimal Number
( 6.35) 8 = ( ? ) 10
=(6 x 80) + (3 x 8-1) + (5 x 8-2)
=(6 x 1) + (3/8) + (5/82)
=6 + 0.375 + 5/64
=6 + 0.375 + 0.078125
= (6.453125)10

## Slide 13: Hexadecimal Number System
Base 16
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Representing Binary in compact form
  11011000001102 = ?

## Slide 14: Hexadecimal Number System
Base 16
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Representing Binary in compact form
  11011000001102 = 1B06 H

## Slide 15: Counting in Hexadecimal
Decimal | Binary | Hexadecimal | Decimal | Binary | Hexadecimal
0 | 0000 | 0 | 8 | 1000 | 8
1 | 0001 | 1 | 9 | 1001 | 9
2 | 0010 | 2 | 10 | 1010 | A
3 | 0011 | 3 | 11 | 1011 | B
4 | 0100 | 4 | 12 | 1100 | C
5 | 0101 | 5 | 13 | 1101 | D
6 | 0110 | 6 | 14 | 1110 | E
7 | 0111 | 7 | 15 | 1111 | F

## Slide 16: Counting in Hexadecimal
Decimal | Hexa- Decimal | Decimal | Hexa- Decimal | Decimal | Hexa- Decimal
16 | 10 | 24 | 18 | 32 | 20
17 | 11 | 25 | 19 | 33 | 21
18 | 12 | 26 | 1A | 34 | 22
19 | 13 | 27 | 1B | 35 | 23
20 | 14 | 28 | 1C | 36 | 24
21 | 15 | 29 | 1D | 37 | 25
22 | 16 | 30 | 1E | 38 | 26
23 | 17 | 31 | 1F | 39 | 27

## Slide 17
(1E) 16 = (?) 10
=(1 x 161) + (E x 160)
=1 x 16 + E x 1
=16 + 14 x1 =16 + 14
=(30) 10
Hexadecimal to Decimal Conversion

## Slide 18
(CA02) 16 = (?) 10
Hexadecimal to Decimal Conversion

## Slide 19: Sum-of-Weights
(CA02) 16 = (?) 10
=(C x 163) + (A x 162) + (0 x 161) + (2 x 160)
=(12 x 163) + (10 x 162) + (0 x 161) + (2 x 160)
=(12 x 4096) + (10 x 256) + (0 x 16) + (2 x 1)
=49152 + 2560 + 0 + 2
=(51714) 10
Hexadecimal to Decimal Conversion

## Slide 20: Sum-of-Weights
(CA02) 16 = (?) 10
=(C x 163) + (A x 162) + (0 x 161) + (2 x 160)
=(12 x 163) + (10 x 162) + (0 x 161) + (2 x 160)
=(12 x 4096) + (10 x 256) + (0 x 16) + (2 x 1)
=49152 + 2560 + 0 + 2
=(51714) 10
Hexadecimal to Decimal Conversion

## Slide 21: Caveman Number System
Decimal Number | Caveman Number | Decimal Number | Caveman Number
0 | ∑ | 10 | >∑
1 | ∆ | 11 | >∆
2 | > | 12 | >>
3 | Ω | 13 | >Ω
4 | ↑ | 14 | >↑
5 | ∆∑ | 15 | Ω∑
6 | ∆∆ | 16 | Ω∆
7 | ∆> | 17 | Ω>
8 | ∆Ω | 18 | ΩΩ
9 | ∆↑ | 19 | Ω↑
Notes: 21
The caveman can represent the first five decimal numbers (0-4) using a single digit of the caveman number system as shown in the table.
To represent higher values (5-9) a combination of two digits is used.
What should be the most significant digit?
Just think, how do you represent a value greater than 9 in the decimal system?
In a decimal number system after counting up to 9, two digits are used. The most significant digit is fixed at the next highest value 1, and the least significant digit varies between 0 and 9 (10 to19). After 19, the most significant digit is set to 2 and the least significant digit varies between 0 and 9 (20-29) and so on.
Thus in the caveman number system the most significant digit is ∆, and the least significant digit varies between ∑ to ↑. The caveman representation of decimal numbers 5 to 9 is shown in the table.
In a decimal number system how do we represent number after 19? The most significant digit is increased to the next value (from 1 to 2) and the least significant varies between 0 and 9.
Thus in the caveman number system same procedure is followed. The table shows the Caveman number system equivalents to the first 20 decimal values.

## Slide 22: Caveman Number System
∑, ∆, >, Ω and ↑
Base – 5 Number System
Notes: 22
Now let us see how numbers can be represented in a new number system.
A number system discovered by archeologists in a prehistoric cave indicates that the caveman used a number system that has 5 distinct symbols ∑, ∆, >, Ω and ↑. (Sigma, Delta, Greater than, Omega and Arrow)
Furthermore it has been determined that the five symbols represents the decimal equivalents of numbers 0 to 4 respectively.
Which number is the Caveman using?
Since there are 5 unique symbols specifying 5 values. Therefore the Caveman is using a Base 5 number system.
The number ∆Ω↑∑ in Base 5 number system represents 220 in decimal.
Before we see how ∆Ω↑∑ represents 220 in decimal, let us see the Caveman Number representations of the decimal number system.

## Slide 23: Caveman Number System to Decimal
Mr. Caveman is a base 5 number system.
( Ω∆ ) 5 = ( ? )10
= Ω x 51 + ∆ x 50
= Ω x 5 + ∆ x 1
= (3) x 5 + (1) x 1
= 15 + 1 = 16
Notes: 23
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 24: Caveman Number System to Decimal
(>↑) 5 = ( ? )10
Notes: 24
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 25: Caveman Number System to Decimal
(>↑) 5 = ( 14 )10
Notes: 25
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 26: Caveman Number System to Decimal
(∆Ω↑∑ ) 5 = ( ? )10
Notes: 26
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 27: Caveman Number System to Decimal
(∆Ω↑∑ ) 5 = ( ? )10
= ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
= ∆ x 125 + Ω x 25 + ↑ x 5 + ∑ x 1
= (1) x 125 + (3) x 25 + (4) x 5 + (0) x 1
= 125 + 75 + 20 + 0 = 220
Notes: 27
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 28: Caveman Number FRACTIONS to Decimal
(Ω ∑. ∆> ) 5 = ( ? )10
Notes: 28
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 29: Caveman Number FRACTIONS to Decimal
(Ω ∑. ∆> ) 5 = ( ? )10
= Ω x 51 + ∑ x 50 + ∆ x 5-1 + > x 5-2
= Ω x 5 + ∑ x 1 + ∆ /5 + > /5-2
= 3 x 5 + 0 x 1 + 1/ 5 + 2/25
=15 + 0 + 0.2 + 0.08 = (15.28)10
Notes: 29
Let us see how the caveman number ∆Ω↑∑ represent 220 in decimal.
The number ∆Ω↑∑ can be easily converted into decimal if we write an expression for the Caveman number ∆Ω↑∑ in terms of the base number and the weights.
What is the base number of the caveman number system? 5.
What is the weight of the most significant digit of the number ∆Ω↑∑? 53
Similarly the weights of the digits Ω, ↑ and ∑ are 52, 51 and 50 respectively.
The weights of the four digits starting from the most significant digit are 125, 25, 5 and 1
The weights change by a factor 5.
Thus writing the number ∆Ω↑∑ in terms of an expression is ∆ x 53 + Ω x 52 + ↑ x 51 + ∑ x 50
Replacing the caveman numbers by their decimal equivalents changes the expression to 1 x 53 + 3 x 52 + 4 x 51 + 0 x 50
Solving the expression gives four terms 125, 75, 20 and 0. Adding the four terms gives the result 220.

## Slide 30: Binary Number System
Two unique numbers 0 and 1
Base – 2
A binary digit is a bit
Combination of bits to represent larger values
Notes: 30
Digital systems as mentioned earlier use a Binary number system.
Binary as the name indicates is a base 2 number system having only two values 0 and 1.
A binary digit is known as a Bit.
Similar to other number systems the Binary Number System uses a combination of digits or Bits to represent numbers larger than 0 and 1.
Lets have a look at Binary Representation of Decimal Numbers.

## Slide 31: Binary Number System
Decimal Number | Binary Number | Decimal Number | Binary Number
0 | 0 | 10 | 1010
1 | 1 | 11 | 1011
2 | 10 | 12 | 1100
3 | 11 | 13 | 1101
4 | 100 | 14 | 1110
5 | 101 | 15 | 1111
6 | 110 | 16 | 10000
7 | 111 | 17 | 10001
8 | 1000 | 18 | 10010
9 | 1001 | 19 | 10011
Notes: 31
A single binary bit can represent only two decimal values 0 and 1.
To represent the next two decimal values, two binary bits are used. The most significant bit remains fixed at 1 and the least significant bit changes between 0 and 1. Thus decimal numbers 2 and 3 are represented by two bit binary numbers 10 and 11 respectively.
How are the decimal numbers 4 and 5 represented?
The decimal numbers 4 and 5 are represented by a combination of 3 bits. The most significant two bits remain fixed and the least significant bit changes between 0 and 1.
Higher decimal numbers can be represented in binary by using a larger combination of bits.
The Binary representations of the first 20 decimal numbers are shown in the table.

## Slide 32: Conversion Binary to Decimal
100112 = (?)10
Notes: 32
Don’t worry, if you have not understood the binary representation. We would be discussing binary numbers through the course.
Let us find out what does the Binary combination 100112 represent? It represents the decimal number 19.
Let us see how the Binary number 100112 represent decimal 19?
The decimal equivalent of a combination of binary number can easily be found by writing an expression in terms of the base value and weights as we did earlier with the caveman number system.
What is the base number of binary number system? 2
What are the weights of the 5 bits 10011? Starting from the most significant left most bit the weights are 24, 23, 22, 21 and 20.
Writing an expression in terms of the binary bits and the respective weights results in the expression (1 x 24) + (0 x 23) + (0 x 22) + (1 x 21) + (1 x 20)
Solving the expression results in five terms 16, 0, 0, 2 and 1, which sum up to 19.
The subscript 2 indicates that the number 10011 is binary and not decimal ten thousand eleven.
The weights of the 5 bits starting from the left, most significant bit are 16, 8, 4, 2 and 1.
The weights in a Binary Number system change by a factor of two.
The most significant bit on the extreme left has the highest weight.
In the decimal number and the caveman number system the weights increased by a factor of 10 and 5 respectively.

## Slide 33: Conversion Binary to Decimal
100112 = (?)10
= (1 x 24) + (0 x 23) + (0 x 22) + (1 x 21) + (1 x 20)
= (1 x 16) + (0 x 8) + (0 x 4) + (1 x 2) + (1 x 1)
= 16 + 0 + 0 + 2 + 1
= (19)10
Notes: 33
Don’t worry, if you have not understood the binary representation. We would be discussing binary numbers through the course.
Let us find out what does the Binary combination 100112 represent? It represents the decimal number 19.
Let us see how the Binary number 100112 represent decimal 19?
The decimal equivalent of a combination of binary number can easily be found by writing an expression in terms of the base value and weights as we did earlier with the caveman number system.
What is the base number of binary number system? 2
What are the weights of the 5 bits 10011? Starting from the most significant left most bit the weights are 24, 23, 22, 21 and 20.
Writing an expression in terms of the binary bits and the respective weights results in the expression (1 x 24) + (0 x 23) + (0 x 22) + (1 x 21) + (1 x 20)
Solving the expression results in five terms 16, 0, 0, 2 and 1, which sum up to 19.
The subscript 2 indicates that the number 10011 is binary and not decimal ten thousand eleven.
The weights of the 5 bits starting from the left, most significant bit are 16, 8, 4, 2 and 1.
The weights in a Binary Number system change by a factor of two.
The most significant bit on the extreme left has the highest weight.
In the decimal number and the caveman number system the weights increased by a factor of 10 and 5 respectively.

## Slide 34: Binary FRACTIONS to Decimal
1011.1012 = (?)10
Notes: 34
Both integers and fractions can be represented in the Binary number system just like in the decimal number system.
The number 1011.1012 is equivalent to decimal 11.625
Let us see how?
Calculating the decimal equivalent of a binary number representing a fraction can easily be done by writing the expression in terms of the base value and weights as was done in the case of integer numbers.
The binary number 1011.1012 has an integer part 1011 having the weights 23, 22, 21 and 20.
The fraction part 101 has the weights 2-1, 2-2 and 2-3.
The weights of the fraction part of the binary number decrease by a factor of 2 starting from the bit immediately to the right of the decimal point.
(1 x 23) + (0 x 22) + (1 x 21) + (1 x 20) + (1 x 2-1) + (0 x 2-2) + (1 x 2-3)
Multiplying the weights with the corresponding decimal equivalents of the binary bits results in the terms 8, 0, 2, 1, 0.5, 0 and 0.125 which add up to give 11.625
One last word on binary representation of fractions. Computers do handle numbers such as 11.625 that have an integer part and a fraction part. However, it does not use the binary representation 1011.101. Such numbers are represented and used in Floating-Point Numbers notation which will be discussed latter

## Slide 35: Binary FRACTIONS to Decimal
1011.1012 = (?)10
  = (1 x 23) + (0 x 22) + (1 x 21) + (1 x 20)
  + (1 x 2-1) + (0 x 2-2) + (1 x 2-3)
  = (1 x 8) + (0 x 4) + (1 x 2) + (1 x 1)
  + (1 x 1/2) + (0 x 1/4) + (1 x 1/8)
  = 8 + 0 + 2 + 1 + 0.5 + 0 + 0.125
  = 11.625
Notes: 35
Both integers and fractions can be represented in the Binary number system just like in the decimal number system.
The number 1011.1012 is equivalent to decimal 11.625
Let us see how?
Calculating the decimal equivalent of a binary number representing a fraction can easily be done by writing the expression in terms of the base value and weights as was done in the case of integer numbers.
The binary number 1011.1012 has an integer part 1011 having the weights 23, 22, 21 and 20.
The fraction part 101 has the weights 2-1, 2-2 and 2-3.
The weights of the fraction part of the binary number decrease by a factor of 2 starting from the bit immediately to the right of the decimal point.
(1 x 23) + (0 x 22) + (1 x 21) + (1 x 20) + (1 x 2-1) + (0 x 2-2) + (1 x 2-3)
Multiplying the weights with the corresponding decimal equivalents of the binary bits results in the terms 8, 0, 2, 1, 0.5, 0 and 0.125 which add up to give 11.625
One last word on binary representation of fractions. Computers do handle numbers such as 11.625 that have an integer part and a fraction part. However, it does not use the binary representation 1011.101. Such numbers are represented and used in Floating-Point Numbers notation which will be discussed latter

## Slide 36: Binary to Decimal Conversion
Sum-of-Weights
  Expression base number & weights
  Sum terms
  Paper and pencil method
Sum of non-zero terms
  Mental Arithmetic, quick method
  Sum of weights of non-zero terms
Notes: 36
Lets first look at the conversion from binary number system to decimal number system.
In the last lecture I had mentioned that there are two methods to convert a binary number to decimal.
The Sum-of-Weights method and the sum of non-zero terms.
Let's consider both methods.
We have already been converting binary numbers to decimal using the Sum-of-Weights.
Converting the binary number 100112 using the Sum-of-Weights method requires writing an expression in terms of the base number and weights.
(1 x 24) + (0 x 23) + (0 x 22) + (1 x 21) + (1 x 20)
Solving the expression results in the terms 16, 0, 0, 2 and 1 which add up to 19.

## Slide 37: Binary to Decimal Conversion
Add weights of non-zero terms
Weights increase/decrease by power of 2
100112 = 16 + 2 + 1 = 19
1011.1012 = 8 + 2 + 1 + 1/2 + 1/8
= 11 + 5/8
= 11.625
Notes: 37
A quicker method is to add the weights of non-zero terms.
What are the weights of the non-zero terms for the binary number 100112?
If you remember the weight of the binary bits increase by a factor of two starting from the least significant bit.
Thus, the weights of non-zero terms are 16, 2 and 1. Adding the weights of non-zero terms results in 19.
Adding the weights of non-zero terms involves mental arithmetic and is quick way of converting binary numbers into decimal.
Consider another example of converting 1011.1012 to decimal using sum of non-zero terms.
The weights of the non-zero terms are 8, 2, 1, ½ and 1/8 which add up to 11.625.
You should practice the adding of non-zero terms to find decimal equivalents of binary numbers as it is a convenient and quick way to convert binary into decimal.

## Slide 38: Decimal to Octal Conversion
Number | Quotient | Remainder
2075/8 | =259.375 | =0.375 x 8 = 3 (O0)
Repeated Division by 8
(2075)10 =( ?) 8

## Slide 39: Decimal to Octal Conversion
Number | Quotient | Remainder
2075 | =259 | =0.375 x 8 = 3 (O0)
259/8 |  | 
Repeated Division by 8
(2075)10 =( ?) 8

## Slide 40: Decimal to Octal Conversion
Number | Quotient | Remainder
2075 | =259 | =0.375 x 8 = 3 (O0)
259/8 | =32 | =0.375 x 8 = 3 (O1)
Repeated Division by 8
(2075)10 =( ?) 8

## Slide 41: Decimal to Octal Conversion
Number | Quotient | Remainder
2075 | =259 | =0.375 x 8 = 3 (O0)
259 | =32 | =0.375 x 8 = 3 (O1)
32/4 | =4 | =0 x 8 = 0 (O2)
Repeated Division by 8
(2075)10 =( ?) 8

## Slide 42: Decimal to Octal Conversion
Number | Quotient | Remainder
2075 | =259 | =0.375 x 8 = 3 (O0)
259 | =32 | =0.375 x 8 = 3 (O1)
32 | =4 | =0 x 8 = 0 (O2)
4 | =0 | = 0.5 x 8= 4 (O3)
Repeated Division by 8
(2075)10 =( ?) 8

## Slide 43: Decimal to Octal Conversion
Number | Quotient | Remainder
Repeated Division by 8
(3182)10 =( ?) 8
Notes: 6156

## Slide 44: Repeated Division by 16
Number | Quotient | Remainder
2096/16 |  | 
Decimal to Hexadecimal Conversion
(2096)10 =( ? ) 16

## Slide 45: Repeated Division by 16
Number | Quotient | Remainder
2096 | 131 | =0x 16 = 0 (O0)
Decimal to Hexadecimal Conversion

## Slide 46: Repeated Division by 16
Number | Quotient | Remainder
2096 | 131 | =0x 16 = 0 (O0)
131/16 |  | 
Decimal to Hexadecimal Conversion

## Slide 47: Repeated Division by 16
Number | Quotient | Remainder
2096 | 131 | =0x16 = 0
131 | 8 | =0.1875x16=3
Decimal to Hexadecimal Conversion
(2096)10 =( ? ) 16

## Slide 48: Repeated Division by 16
Number | Quotient | Remainder
2096 | 131 | =0x 16= 0 (O0)
131 | 8 | =0.1875x16=3 (O1)
8/16 | 0 | =0.5 x16= 8 (O2)
Decimal to Hexadecimal Conversion
(2096)10 =( ? ) 16

## Slide 49: Repeated Division by 16
Number | Quotient | Remainder
2096 | 131 | =0x 16= 0 (O0)
131 | 8 | =0.1875x16=3 (O1)
8 | 0 | =0.5 x16= 8 (O2)
Decimal to Hexadecimal Conversion
(2096)10 =( ? ) 16

## Slide 50: Repeated Division by 16
Number | Quotient | Remainder
Decimal to Hexadecimal Conversion
(3182)16 =( ? ) 10
Notes: C6E

## Slide 51: Decimal to CAVEMAN Conversion
Number | Quotient | Remainder
220 | =44 | =0 x 5 = 0 (∑) (O0)
44 | =8 | =0.8 x 5 = 4 (↑) (O1)
8 | =1 | =0.6 x 5 = 3(Ω) (O2)
1 | =0 | = 0.2 x 5= 1(∆) (O3)
Repeated Division by 8
(220)10 =( ?) 5

## Slide 52: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
Notes: 52
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 53: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
Notes: 53
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 54: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
Notes: 54
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 55: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
49 | 24 | 1 (b3)
Notes: 55
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 56: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
49 | 24 | 1 (b3)
24 | 12 | 0 (b4)
Notes: 56
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 57: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
49 | 24 | 1 (b3)
24 | 12 | 0 (b4)
12 | 6 | 0 (b5)
Notes: 57
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 58: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
49 | 24 | 1 (b3)
24 | 12 | 0 (b4)
12 | 6 | 0 (b5)
6 | 3 | 0 (b6)
Notes: 58
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 59: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
49 | 24 | 1 (b3)
24 | 12 | 0 (b4)
12 | 6 | 0 (b5)
6 | 3 | 0 (b6)
3 | 1 | 1 (b7)
Notes: 59
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 60: Decimal to Binary Conversion Repeated division by 2
number | Quotient after division | Remainder after division
392 | 196 | 0 (b0)
196 | 98 | 0 (b1)
98 | 49 | 0 (b2)
49 | 24 | 1 (b3)
24 | 12 | 0 (b4)
12 | 6 | 0 (b5)
6 | 3 | 0 (b6)
3 | 1 | 1 (b7)
1 | 0 | 1 (b8)
Notes: 60
Repeated Division-by-2 method allows decimal numbers of any magnitude to be converted into binary.
The original number is divided by 2, its quotient and the remainder is noted.
The quotient obtained in the first step is again divided and the new quotient and remainder value noted.
The process of repeatedly dividing the previous quotient value and noting the remainder continues until the quotient value becomes 0.
The remainders noted in the repeated division are written out in reverse to represent the binary equivalent of the decimal number.
110001000

## Slide 61: Binary FRACTION to -Decimal FRACTION
Decimal to Binary Conversion
  Repeated Multiplication by 2
Notes: 61
Converting fractions in decimal number system to Binary and vice versa is also important.
Binary to Decimal conversion uses the Sum-of Weight method used earlier.
The weight of binary bits constituting the fraction part decreases by a factor of 2 starting from the bit to the immediate left of the decimal point.
Thus 0.11012 has the weights ½, ¼ and 1/16 for the non-zero terms.
Adding the non-zero term weights results in 13/16 or 0.8125

## Slide 62: Decimal-Binary fraction conversion
Decimal to Binary Conversion
  Repeated multiplication by 2
Number | Mult. By 2 | Integer
0.8125 | 1.625 | 1 (b-1)
Notes: 62
Converting fractions from decimal to binary requires repeated multiplication by 2.
The decimal number 0.8125 to be converted into binary is multiplied by 2 which results in 1.625.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 1.250.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 0.5.
The integer part ‘0’ is noted and the fraction part is multiplied by 2. The result is 1.
Since the fraction part is 0, therefore there is no further need for multiplying with 2.
The integer part is noted and the noted integer values are written out preceded by a decimal point to give 0.1101

## Slide 63: Decimal-Binary fraction conversion
Decimal to Binary Conversion
  Repeated multiplication by 2
Number | Mult. By 2 | Integer
0.8125 | 1.625 | 1 (b-1)
0.625 | 1.250 | 1 (b-2)
Notes: 63
Converting fractions from decimal to binary requires repeated multiplication by 2.
The decimal number 0.8125 to be converted into binary is multiplied by 2 which results in 1.625.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 1.250.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 0.5.
The integer part ‘0’ is noted and the fraction part is multiplied by 2. The result is 1.
Since the fraction part is 0, therefore there is no further need for multiplying with 2.
The integer part is noted and the noted integer values are written out preceded by a decimal point to give 0.1101

## Slide 64: Decimal-Binary fraction conversion
Decimal to Binary Conversion
  Repeated multiplication by 2
Number | Mult. By 2 | Integer
0.8125 | 1.625 | 1 (b-1)
0.625 | 1.250 | 1 (b-2)
0.250 | 0.500 | 0 (b-3)
Notes: 64
Converting fractions from decimal to binary requires repeated multiplication by 2.
The decimal number 0.8125 to be converted into binary is multiplied by 2 which results in 1.625.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 1.250.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 0.5.
The integer part ‘0’ is noted and the fraction part is multiplied by 2. The result is 1.
Since the fraction part is 0, therefore there is no further need for multiplying with 2.
The integer part is noted and the noted integer values are written out preceded by a decimal point to give 0.1101

## Slide 65: Decimal-Binary fraction conversion
Decimal to Binary Conversion
  Repeated multiplication by 2
Number | Mult. By 2 | Integer
0.8125 | 1.625 | 1 (b-1)
0.625 | 1.250 | 1 (b-2)
0.250 | 0.500 | 0 (b-3)
0.500 | 1.000 | 1 (b-4)
(0.8125)10=(0.1101)2
Notes: 65
Converting fractions from decimal to binary requires repeated multiplication by 2.
The decimal number 0.8125 to be converted into binary is multiplied by 2 which results in 1.625.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 1.250.
The integer part ‘1’ is noted and the fraction part is multiplied by 2. The result is 0.5.
The integer part ‘0’ is noted and the fraction part is multiplied by 2. The result is 1.
Since the fraction part is 0, therefore there is no further need for multiplying with 2.
The integer part is noted and the noted integer values are written out preceded by a decimal point to give 0.1101

## Slide 66: More conversions?
Decimal to Octal Fraction?
Decimal to Hexa Fraction?

## Slide 67: Binary Arithmetic
Binary Addition
Binary Subtraction
Binary Multiplication
Binary Division
Notes: 67
We have looked at binary to decimal conversions and decimal to binary conversions.
Now we know how to convert integers as well as fractions from one number system to the other.
Now lets look at simple arithmetic operations such as add, subtract, multiply and divide.
We should be able to perform simple arithmetic operations such as add, subtract, multiply and divide on binary numbers, as we normally do with decimal numbers.
Arithmetic operations performed on binary numbers are in fact exactly like the operations performed on decimal numbers.
Let us start by looking at the binary addition operation

## Slide 68: Binary Addition
Four Basic rules for binary addition
1st digit | 2nd digit | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Addition of multiple binary numbers
Notes: 68
Looking at the results the first three additions give a result 0, 1 and 1 respectively which can be represented by a single binary digit (bit).
The fourth addition results in the number 2, which is represented in binary as 102.
Thus two digits (bits) are required. The sum bit is 0 and the carry bit is 1.
This is similar to the addition of 9 + 3 in decimal. The answer is 12 which can not be represented by a single digit, thus two digits are required. The number 2 is the sum part and 1 is the carry part.

## Slide 69: Binary Addition
Carry | 1 | 1 | 10 | 1 | 
1st Number |  | 1 | 0 | 1 | 1
2nd Number |  |  | 1 | 1 | 0
3rd Number |  | 1 | 0 | 0 | 0
4th Number |  |  |  | 1 | 1
Result | 1 | 1 | 1 | 0 | 0
Notes: 69
Similar to Decimal addition any number of binary numbers having any number of digits can be added together.
Thus the number 1011, 110, 1000 and 11 can be added together. Most significant digits (bits) of second and fourth numbers are assumed to be zero.
At Bit 2 the carry is 10, is it possible to have a 2-bit carry?
Consider adding the number 19, fifteen times.
Adding the first digit 9, fifteen times results in 135. 5 is the Sum and 13 is the carry.
The carry 13 added with fifteen 1s of the second digit result in 28.
The answer is 285.

## Slide 70: Binary Subtraction
Four Basic rules for binary subtraction
1st digit | 2nd digit | Difference | Borrow
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Notes: 70
The 2nd digit is subtracted from the first.
The result of the first, third and fourth subtraction operations result in a difference value where no borrow is required.
The second subtraction subtracts 1 from 0 for which a borrow is required to make the first digit equal to 2. The answer is 1.
This is similar to what is done in decimal 21-17 where 7 can not be subtracted from 1 therefore a 1 is borrowed from the next most significant digit to allow 7 to be subtracted from 11.
Thus if only the least significant digit of the decimal numbers is considered subtracting 7 from 1 results in a borrow of 1 and a difference of 4.

## Slide 71: Binary Subtraction
Borrow |  |  | 1 |  | 
1st Number |  | 1 | 0 | 1 | 1
2nd Number |  |  | 1 | 1 | 0
Result |  |  | 1 | 0 | 1
Notes: 71

## Slide 72: Binary Multiplication
Four Basic rules for binary multiplication
1st digit | 2nd digit | Product
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Example of Binary Multiplication
Notes: 72
In binary multiplication anything multiplied by 0 results in 0 just like in decimal multiplication.

## Slide 73: Binary Multiplication
1101 (13)
x 101 (5)
1st product term 1101
2nd product term 0000x
3rd product term 1101xx
Product 1000001 (65)
Notes: 73
Binary multiplication is identical to the decimal multiplication.
The first product term results in 1101
The second product term results in 0000 and is written shifted left by 1 bit
The third product term results in 1101 and is written shifted left by 2 bits
The product result is sum of all the partial product terms

## Slide 74: Multiplication by shifting left
Decimal 29 shifted left by one digit
290
Shift left 1 digit is multiply by 10
Binary 111012 (29) shifted left by one bit
1110102 (58)
Shift left 1 bit is multiply by 2
Notes: 74
Multiplication operations can be performed by shifting a number towards left.
For example decimal 29 shifted left by 1 digit is like multiplying by 10
Shifting 29 by two digits towards left is multiplying by 102 or 100
Each shift left operation in decimal is equivalent to multiplying a number by 10.
In a binary number system, each left shift is equivalent to multiplying by 2.
Shifting 111012 twice towards left is 11101002 which is multiply by 4.

## Slide 75: Binary Division(OPTIONAL)
10
101 | 1101
101
011
000
11
2
5 | 13
10
3
Notes: 75
Binary division follows the same rules as in decimal division.
https://www.youtube.com/watch?v=KGMf314LUc0&t=508s
https://www.youtube.com/watch?v=LGqBQrUYua4
https://www.youtube.com/watch?v=HdU_rf7eMTI
The binary division divides 11012 (13) by 1012 (5) which results in a quotient value of 102 (2) and a remainder 112 (3) which is in confirmation with equivalent decimal division.

## Slide 76: Binary Division(OPTIONAL)
10
11 | 110
110
0
11
10 | 110 10
10
10
0
Notes: 76
Binary division follows the same rules as in decimal division.
The binary division divides 11012 (13) by 1012 (5) which results in a quotient value of 102 (2) and a remainder 112 (3) which is in confirmation with equivalent decimal division.

## Slide 77: Division by shifting right
Decimal 29 shifted right by one digit
2.9
Shift left 1 digit is divide by 10
Binary 111012 (29) shifted left by one bit
1110.12 (14.5)
Shift left 1 bit is divide by 2
Notes: 77
Division operations can be performed by shifting a number towards right.
For example decimal 29 shifted right by 1 digit is like dividing by 10
Shifting 29 by two digits towards right is dividing by 102 or 100
Each shift right operation in decimal is equivalent to dividing a number by 10.
In a binary number system, each right shift is equivalent to dividing by 2.
Shifting 111012 twice towards right is 111.012 which is divide by 4.