## Slide 1: Digital Logic & Design Lecture 05
Notes: 1

## Slide 2: Logic Gates
Basic Building Blocks
Logic Gate Symbol
Unique function
Truth or Function Table
Function Expression
Timing Diagram

## Slide 3: AND Gate
1 output
2 inputs
3 inputs
4 inputs
Multiple inputs

## Slide 4: AND Gate function
Logical Multiplication function
Input |  | Output
A | B | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5: AND Gate Timing Diagram

## Slide 6: AND Gate function

## Slide 7: AND Gate Applications
Enable/Disable Device
  Counter counts when it receives pulses

## Slide 8: OR Gate
1 output
2 inputs
3 inputs
4 inputs
Multiple inputs

## Slide 9: OR Gate function
Boolean Add function
Input |  | Output
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: OR Gate Timing Diagram

## Slide 11: OR Gate Applications
Car door open alarm

## Slide 12: NOT Gate
1 input
1 output

## Slide 13: NOT Gate function
Invert function
Input | Output
A | F
0 | 1
1 | 0

## Slide 14: NOT Gate Timing Diagram

## Slide 15: NOT Gate Applications
1’s Complement

## Slide 16: Alternate Representations

## Slide 17: NAND Gate
1 output
2 inputs
3 inputs
4 inputs
Multiple inputs

## Slide 18: NAND Gate function
NOT-AND function
Input |  | Output
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 19: NAND Gate Timing Diagram

## Slide 20: NAND Universal Gate
Input |  | Output
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 21: NAND Universal Gate
Input |  | Output | Output
A | B | F1 | F
0 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 22: NAND Universal Gate
Input |  | Output
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 23: NAND Gate Applications
Device Failure Alarm
Notes: 23
Toxic fumes produced by the chemicals are removed from the warehouse and dispersed in the atmosphere through three exhaust fans.
When all fans are working the input to the NAND gate is 111 and the output is 0
When any one fan fails the output of NAND gate becomes 1 sounding an alarm connected tot the output of the NAND gate.

## Slide 24: NOR Gate
1 output
2 inputs
3 inputs
4 inputs
Multiple inputs

## Slide 25: NOR Gate function
NOT-OR function
Input |  | Output
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 26: NOR Gate Timing Diagram

## Slide 27: NOR Universal Gate
Input |  | Output
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 28: NOR Universal Gate
Input |  | Output
A | B | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 29: NOR Gate Applications
Washing Machine Controller
Notes: 29
Three sensors check for washing machine lid open, washing tub filled to minimum level and weight of cloths and water in the tub.
If the lid is open or the water is below the minimum level, or the washing machine has been overloaded the appropriate sensor sets its output to 1. The NOR gate output is set to 0 switching off the washing machine.

## Slide 30: NAND-NOR Universal Gate

## Slide 31: XOR Gate
1 output
2 inputs
Multiple inputs

## Slide 32: XOR Gate function
Input |  | Output
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 33: XOR Gate Timing Diagram

## Slide 34: XOR Gate Applications
Detecting odd number of 1’s
Notes: 34
Consider the three XOR gate logic circuit which is used to detect odd number of 1’s in a 4-bit binary input combination
Consider the 4-bit binary number 0000 applied at the inputs A, B, C and D respectively of XOR gates 1 and 2.
The output of XOR Gates 1 and 2 is 0 and 0. The output of XOR gate 3 is also zero.
Consider the binary number 0011 applied at the inputs A, B, C and D respectively. The output of XOR gate 1 with inputs 00 is 0. The output of XOR gate 2 with inputs 11 is 0. The output of gate 3 is 0. Thus the output indicates that the binary number 0011 does not have odd number of 1’s
Consider the binary number 1011 applied at the inputs A, B, C and D respectively. The output of XOR gate 1 with inputs 10 is 1. The output of XOR gate 2 with inputs 11 is 0. The output of gate 3 is 1. Thus the output indicates that the binary number 1011 has odd number of 1’s

## Slide 35: XNOR Gate
1 output
2 inputs
Multiple inputs

## Slide 36: XNOR Gate function
Input |  | Output
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 37: XNOR Gate Timing Diagram

## Slide 38: XNOR Gate Applications
Detecting even number of 1’s
Notes: 38
Consider the two XOR and a single XNOR gate based logic circuit used to detect even number of 1’s in a 4-bit binary input combination
Consider the 4-bit binary number 0000 applied at the inputs A, B, C and D respectively of XOR gates 1 and 2.
The output of XOR Gates 1 and 2 is 0 and 0. The output of XNOR gate 3 is a 1.
Consider the binary number 0011 applied at the inputs A, B, C and D respectively. The output of XOR gate 1 with inputs 00 is 1. The output of XOR gate 2 with inputs 11 is 1. The output of XNOR gate 3 is also a 1. Thus the output indicates that the binary number 0011 has even number of 1’s
Consider the binary number 1011 applied at the inputs A, B, C and D respectively. The output of XOR gate 1 with inputs 10 is 1. The output of XOR gate 2 with inputs 11 is 0. The output of XNOR gate 3 is 0 because of dissimilar inputs. Thus the output indicates that the binary number 1011 does not have even number of 1’s

## Slide 39: Type of IC Logic Gates
74XX00 Quad 2-input NAND Gate
74XX02 Quad 2-input NOR Gate
74XX04 Hex Inverter
74XX08 Quad 2-input AND Gate
74XX10 Triple 3-input NAND Gate
74XX11 Triple 3-input AND Gate
74XX20 Dual 4-input NAND Gate
Notes: 39
To identify and use the Integrated Circuits or ICs in implementing logic circuits, some sort of identification code has to be used which is printed on the IC package.
Thus the various Logic Gates are identified by the codes shown.
The prefix 74 is used to identify a commercial version of the device from the military version device identified by the prefix 54.
Military versions are designed to withstand harsh and severe environmental conditions.
The XX part of the code identifies the switching speed of the gate.

## Slide 40: Type of IC Logic Gates
74XX21 Dual 2-input AND Gate
74XX27 Triple 3-input NOR Gate
74XX30 Single 8-input NAND Gate
74XX32 Quad 2-input OR Gate
74XX86 Quad 2-input XOR Gate
74XX133 Single 13-input NAND Gate
Notes: 40

## Slide 41: Logic Gate Integrated Circuits
Notes: 41
The Integrated Circuit packages of the seven gates that have been discussed so far are shown.
The 7408 14-pin chip has 4 or Quad, 2-input AND gates. The input pins and the output pins of each of the four gates are shown. To use any one or all four gates the appropriate pins are connected.
Pins 7 and 14 are connected to ground and Supply voltage respectively.
The 7432 14-pin IC package has 4 or Quad, 2-input OR Gates. Connections to the OR gates are identical to those of the 7408 AND gate IC.
The 7404 14-pin chip has 6 or hex, inverters. The input and output connections of each of the 6 NOT gates are shown. Pins 7 and 14 are used for ground and supply voltage respectively.

## Slide 42: Logic Gate Integrated Circuits
Notes: 42
The 7400, Quad, 2-input NAND Gate IC
The 7402, Quad, 2-input NOR Gate IC
The 7486, Quad, 2-input XOR Gate IC
And the 74266, Quad, 2-input XNOR Gate IC are similar.