## Slide 1: Lecture No. 7
Logic Gates
Notes: 1
Asalam O Aleikum students. I am Waseem Ikram.
This is the seventh lecture in a series of 45 lectures on Digital Logic Design.

## Slide 2: TTL/CMOS NOT Gate
+V
CC
+V
V
o/p
V
i
/
p
+V
DD
V
i
/
p
V
o/p
NPN
Transistor
N-Type
MOSFET
P-Type
MOSFET
Notes: 2
The TTL and CMOS implementation of the NOT gate is described.
In the simplified TTL implementation of the NOT gate a transistor switches between logic 1 state and logic 0 state.
When a voltage +V representing logic 1 is applied at the base of the transistor, the transistor is switched on connecting the voltage supply Vcc and the resistor to the ground.
A current flows from the supply to the ground due to which there is a voltage drop equal to the supply voltage Vcc across the resistor.
As a result the output Vo/p is at ground potential or 0 volts which is logic 0. Thus the output of the Transistor circuit is complement of the input.
If the input base of the transistor is connect to 0 volts (logic 0), the transistor is switched off and there is no flow of current from the supply voltage Vcc to the ground through the resistor.
Thus the output of the circuit is at a potential equal to the supply voltage Vcc or logic 1.
The CMOS implementation uses two complementary P-type and N-type MOSFETs or Metal Oxide Field Effect Transistors are used.
When a logic 1 is applied at the Vi/p of the NOT circuit. The P-type MOSFET switches OFF disconnecting the supply voltage Vdd from the output of the NOT circuit. The N-Type MOSFET switches ON, connecting the ground to the output of the NOT circuit. Thus the output of the NOT circuit is at logic 0.
Similarly when a logic 0 is applied at the Vi/p of the NOT circuit. The P-type MOSFET switches ON connecting the supply voltage Vdd to the output of the NOT circuit. The N-Type MOSFET switches OFF, disconnecting the ground from the output of the NOT circuit. Thus the output of the NOT circuit is at logic 1.

## Slide 3: Integrated Circuits (IC)
CMOS Complementary Metal Oxide Logic
TTL Transistor-Transistor Logic
ECL Emitter Coupled Logic
PMOS p-channel MOS transistor
NMOS n-channel MOS transistor
E2CMOS
Notes: 3
CMOS: The most extensively used technology, characterized by low power consumption, switching speed which is slower but comparable to TTL. Has higher chip density than TTL. Due to high input impedance is easily damaged due to accumulated static charge
TTL: Extensively used technology, characterized by fast switching speed and high power consumption
ECL: Used in specialized applications where switching speed is of prime importance, high speed transmission, memories and arithmetic units
PMOS and NMOS: technologies are used in LSI requiring high chip density. Large memories and microprocessors are implemented using these technologies. These ICs have very low power consumption.
E2CMOS: a combination of CMOS and NMOS technologies used to implement Programmable Logic Devices.

## Slide 4: Operational Characteristics
DC Supply Voltage
Noise Margin
Power Dissipation
Frequency Response
Fan Out

## Slide 5: Recap
Integrated Circuits ICs
Transistors
Implementation technologies
Switching speed
Power dissipation
Circuit density

## Slide 6: Recap
Implementation Technologies
CMOS
TTL
ECL
PMOS & NMOS
E2CMOS
Notes: 6
CMOS: The most extensively used technology, characterized by low power consumption, switching speed which is slower but comparable to TTL. Has higher chip density than TTL. Due to high input impedance is easily damaged due to accumulated static charge
TTL: Extensively used technology, characterized by fast switching speed and high power consumption
ECL: Used in specialized applications where switching speed is of prime importance, high speed transmission, memories and arithmetic units
PMOS and NMOS: technologies are used in LSI requiring high chip density. Large memories and microprocessors are implemented using these technologies. These ICs have very low power consumption.
E2CMOS: a combination of CMOS and NMOS technologies used to implement Programmable Logic Devices.

## Slide 7: Operational Characteristics
DC Supply Voltage
Noise Margin
Power Dissipation
Frequency Response
Fan Out

## Slide 8: TTL Series
74 Standard TTL
74S Schottky TTL
74AS Advanced Schottky TTL
74LS Low-Power Schottky TTL
74ALS Advanced Low-Power Schottky TTL
74F Fast TTL
Notes: 8
The Standard, the Schottky, the Advanced Schottky, the Low-Power Schottky, the Advanced Low-Power Schottky and the FAST TTL series are characterized by their switching speed and power dissipation. The Standard TTL is the slowest and consumes more power and the Advanced low power Schottky has the fastest switching speed and low power requirements.

## Slide 9: CMOS Series
5 V CMOS
  74HC and 74HCT High-Speed
  74AC and 74ACT Advanced CMOS
  74AHC and 74AHCT
  Advanced High Speed
3.3 V CMOS
  74LV Low voltage CMOS
  74LVC Low-voltage CMOS
  74ALVC Advanced Low voltage CMOS
Notes: 9
There are two separate CMOS series of Integrated Circuits. The 5 volt series and the newer 3.3 volt CMOS series.
The 3.3 v CMOS series is characterized by fast switching speeds and very low power dissipation as compared to the 5 v CMOS series.

## Slide 10: Noise Margin
i/p & o/p signals have a range of voltages
Voltage ranges exceeded due to external noise
Effect on performance under noisy conditions
Margin of error

## Slide 11: TTL Logic Levels
Notes: 11
At the input of any TTL logic gate a logic high signal ‘1’ or a logic low signal ‘0’ is applied.
The VIH is the input voltage range of Logic high signal with a range of 2 to 5 volts
VIH(min) is the minimum acceptable input range for a logic high signal
The VIL is the input voltage range of Logic low signal with a range of 0 to 0.8 volts
VIL(max) is the maximum acceptable input range for a logic low signal
Similarly the output of any TTL logic gate can be at logic high ‘1’ or logic low ‘0’
The VOH is the output voltage range of Logic high signal with a range of 2.4 to 5 volts
VOH(min) is the minimum acceptable output range for a logic high signal
The VOL is the output voltage range of Logic low signal with a range of 0 to 0.4 volts
VOL(max) is the maximum acceptable output range for a logic low signal
Consider that the output of an And gate is connected to the input of an OR gate
What are the voltage ranges for the two gates?

## Slide 12: CMOS Logic Levels
Notes: 12
At the input of any CMOS 5 volt series logic gate a logic high signal ‘1’ or a logic low signal ‘0’ is applied.
The VIH is the input voltage range of Logic high signal with a range of 3.5 to 5 volts
VIH(min) is the minimum acceptable input range for a logic high signal which is 3.5 volts
The VIL is the input voltage range of Logic low signal with a range of 0 to 1.5 volts
VIL(max) is the maximum acceptable input range for a logic low signal which is 1.5 volts
Similarly the output of any CMOS 5 volt series logic gate can be at logic high ‘1’ or logic low ‘0’
The VOH is the output voltage range of Logic high signal with a range of 4.4 to 5 volts
VOH(min) is the minimum acceptable output range for a logic high signal which is 4.4 volts
The VOL is the output voltage range of Logic low signal with a range of 0 to 0.33 volts
VOL(max) is the maximum acceptable output range for a logic low signal which is 0.33 volts
At the input of any CMOS 3.3 volt series logic gate a logic high signal ‘1’ or a logic low signal ‘0’ is applied.
The VIH is the input voltage range of Logic high signal with a range of 2 to 3.3 volts
VIH(min) is the minimum acceptable input range for a logic high signal which is 2 volts
The VIL is the input voltage range of Logic low signal with a range of 0 to 0.8 volts
VIL(max) is the maximum acceptable input range for a logic low signal which is 0.8 volts
Similarly the output of any CMOS 3.3 volt series logic gate can be at logic high ‘1’ or logic low ‘0’
The VOH is the output voltage range of Logic high signal with a range of 2.4 to 3.3 volts
VOH(min) is the minimum acceptable output range for a logic high signal which is 2,4 volts
The VOL is the output voltage range of Logic low signal with a range of 0 to 0.4 volts
VOL(max) is the maximum acceptable output range for a logic low signal which is o.4 volts
The two CMOS 5 volts and the 3.3 volts series can not be mixed.

## Slide 13: Unpredictable Behaviour due to Noise
Notes: 13
Consider the CMOS 5 volt series AND gate
Input A of the AND gate is permanently connected to logic high of +5 volts.
Input B of the AND gate is connected to the output of some other gate.
The signal at input B of the AND gate can vary between logic 0 and logic 1.
Consider that the input B is at logic high state with VIH = 4.2 volts which is within the valid voltage range of VIH between 5 and 3.5 volts
Consider a voltage generated due to some external noise added to the 4.2 volt signal.
A sharp dip in the input voltage due to the noise brings the input voltage down to 3 volts for a very short duration.
The 3 volt input is below the minimum input voltage limit of 3.5 volts for logic high input voltage.
This dip in the voltage even for a short duration will result in an output of logic low for a short interval of time, which will cause the logic circuit to malfunction.

## Slide 14: Logic Levels and Noise Margin
VNH = VOH(min) – VIH(min)
VNL = VIL(max) – VOL(max)
Notes: 14
Consider two CMOS 5 volt series AND gates connected together.
The first AND gate has both its inputs connected to logic high, therefore the output of the gate is guaranteed to be logic high.
The logic high voltage output of the first AND gate is assumed to be at 4.6 volts well within the valid VOH range of 5-4.4 volts.
Assume the same noise signal (as described earlier) being added to the output signal of the first AND gate.
The sharp dip due to noise brings the VOH voltage down to 3.4 volts with reference to the VOH of 4.6 volts.
3.4 volts is lower than the VIH(min) of 3.5 volts required by the input of the second AND gate. Thus the circuit will malfunction.
Since VOH(min) is guaranteed to be at 4.4 volts therefore a noise signal being added to 4.4 volts can bring VOH voltage down to a minimum of 3.5 volts which is the acceptable minimum range for VIH
Anything below 3.5 will cause the second gate to malfunction.

## Slide 15: Logic Levels and Noise Margin
CMOS Noise Margins
  VNH = VOH(min) – VIH(min) = 4.4 - 3.5 = 0.9 v
  VNL = VIL(max) – VOL(max) = 1.5 – 0.33 = 1.17 v
  VNH = VOH(min) – VIH(min) = 2.4 – 2.0 = 0.4 v
  VNL = VIL(max) – VOL(max) = 0.8 – 0.4 = 0.4 v
TTL Noise Margins
  VNH = VOH(min) – VIH(min) = 2.4 - 2.0 = 0.4 v
  VNL = VIL(max) – VOL(max) = 0.8 – 0.4 = 0.4 v

## Slide 16: Power Dissipation
Power Dissipation constant for TTL
Power Dissipation varies with frequency for CMOS

## Slide 17: TTL Power Dissipation
Gate Output High (ICCH)
Gate Output Low (ICCL)
Average Power Dissipated
Pcc = Vcc Icc
Pcc = Vcc (ICCH + ICCL)/2

## Slide 18: TTL Power Dissipation

## Slide 19: CMOS Power Dissipation
Power Dissipation varies with frequency for CMOS
PD = (CPD+ CL).VDD2.f
CPD is the internal power dissipation capacitance
CL is the external load dissipation capacitance
VDD is the supply voltage
f is the transition frequency of the output signal
Notes: 19
The power dissipation of a HCMOS gate is 2.75 μW under static conditions and 170 μW at 100 KHz.

## Slide 20: Propagation Delay and Frequency Response
Propagation Delay
Limits frequencies at which gate can operate
Notes: 20
The Propagation Delay of a gate limits the frequencies at which the gate can work. Larger the Propagation Delay lower is the frequency at which the gate can operate. Smaller the Propagation Delay higher the frequency at which the gate can operate.
A Gate with a delay of 3 nsec is faster than a gate with a 10 nsec delay.

## Slide 21: Propagation Delay
tPHL tPLH
Notes: 21
Propagation Delays for logic gates are specified by tPHL and tPLH parameters
The NOT gate is shown
The output of the NOT gate changes from high to low after a delay of time specified by tPHL after the input changes from low to high.
The output of the NOT gate changes from low to high after a delay of time specified by tPLH after the input changes from high to low
The delay time is measured at the 50% transition mark.

## Slide 22: Propagation Delay
Notes: 22
The AND gate is shown. The input B of the AND gate is permanently connected to H, where as input A varies between H and L.
The output of the AND gate changes from low to high after a delay of time specified by tPLH after the input changes from low to high.
The output of the AND gate changes from high to low after a delay of time specified by tPHL after the input changes from high to low
The delay time is measured at the 50% transition mark.

## Slide 23: Speed-Power Product (SPP)
SPP = tP PD
Expressed in Joules (J) units of energy
Lower the SP product better is the performance

## Slide 24: Fan-Out
Number of same series gates that a gate can drive.
Fan-Out for TTL circuits is fixed
Fan-Out for CMOS circuits is related to operational frequency.
Fan-Out decreases with increased frequency

## Slide 25: Fan-Out for TTL Loads
Unit Loads = IOH/IIH = IOL/IIL
= 400 μA/40 μA = 16 mA/1.6 mA = 10
Notes: 25
The fan-out of a logic gate is the maximum number of inputs of the same series in an IC family that can be connected to a gate’s output and still maintain the output voltage levels within the specified limits.
The output current at logic high is IOH = 400 μA
The input current at logic high is IIH = 40 μA
Thus a gate at logic high can source current to another gate connected to its output.
Similarly
The output current at logic low is IOL = 16 mA
The input current at logic low is IIL = 1.6 mA
Thus a gate output at logic low can sink current from another gate connected to its output.
To calculate the unit load that can be connected the Unit load formula is used
Unit Loads = IOH/IIH = IOL/IIL = 400 μA/40 μA = 16 mA/1.6 mA = 10

## Slide 26: Fan-Out for TTL Loads
Notes: 26
Considering that
The output current at logic high is IOH = 400 μA
The input current at logic high is IIH = 40 μA
A gate’s output can be connected to inputs of a maximum of 10 gates as 400 μA can be equally distributed amongst 10 gates that is 40 μA each.

## Slide 27: Fan-Out for TTL Loads
Notes: 27
Similarly considering that
The output current at logic low is IOL = 16 mA
The input current at logic low is IIL = 1.6 mA
A gate’s output can be connected to inputs of a maximum of 10 gates as 1.6 mA from each of the 10 gates can be sunk by it, that is 16 mA
Unit Loads = IOH/IIH = IOL/IIL = 400 μA/40 μA = 16 mA/1.6 mA = 10

## Slide 28: Fan-Out for CMOS Loads
Notes: 28
CMOS loading is different from TTL loading as the type of transistors used in CMOS circuits presents a capacitive load to the driving gate.
When the output of the driving gate is high the input capacitance of the load gate is charging and when the output of the driver gate is low the load gate is discharging.
When more load gates are added the input capacitance increases as input capacitances are being connected in parallel. With the increase in the capacitance, charging and discharging time increases, reducing the maximum frequency at which the gate can operate.
Therefore the fan-out of a CMOS gate depends upon the maximum frequency of operation. Fewer the load gates greater the maximum frequency of operation.

## Slide 29: TTL Series
 | 74 | 74S | 74LS | 74AS | 74ALS | 74F
Performance Rating |  |  |  |  |  | 
Propagation Delay (ns) | 9 | 3 | 9.5 | 1.7 | 4 | 3
Power Dissipation (mW) | 10 | 20 | 2 | 8 | 1.2 | 6
Speed-Power product (pJ) | 90 | 60 | 19 | 13.6 | 4.8 | 18
Max. Clock Rate (MHz) | 35 | 125 | 45 | 200 | 70 | 100
Fan-out (same series) | 10 | 20 | 20 | 40 | 20 | 33

## Slide 30: CMOS Series
 | 74HC | 74AC | 74AHC
Propagation Delay (ns) | 18 | 5 | 3.7
Power Dissipation (mW) Static | 0.00275 | 0.0055 | 0.00275
Power Dissipation (mW) at 100KHz | 0.0625 | 0.08 | 0.0625
Speed-Power product (pJ) at 100KHz | 1.125 | 0.4 | 0.23
Max. Clock Rate (MHz) | 50 | 160 | 170
 | 74LV | 74LVC | 74ALVC
Propagation Delay (ns) | 9 | 4.3 | 3
Power Dissipation (mW) Static | 0.0016 | 0.0008 | 0.0008
Max. Clock Rate (MHz) | 90 | 100 | 150