## Slide 1
Digital Logic & Design
Lecture 12

## Slide 2: Comparator Circuit
Inputs two 2-bit binary numbers A and B
Has three outputs
A>B
A=B
A<B

## Slide 3: Function Table for A>B
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A>B
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A>B
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0
Notes: 3
The function table for the output A>B represents the output of the circuit output logic line representing A>B for 16 combinations of the 2-bit numbers A and B.
The input numbers A and B are represented by A1A0 and B1B0 columns of the function table
Output A>B line is set to 1 when A>B.
Thus for input combinations of A and B that is 01 00, 10 00, 10 01, 11 00, 11 01 and 11 10 the output A>B is 1

## Slide 4: Function Table for A=B
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A=B
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A=B
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Notes: 4
The function table for the output A=B represents the output of the circuit logic line representing A=B for 16 combinations of the 2-bit numbers A and B.
The input numbers A and B are represented by A1A0 and B1B0 columns of the function table
Output A=B line is set to 1 when A=B.
Thus for input combinations of A and B that is 00 00, 01 01, 10 10 and 11 11 the output A=B is 1

## Slide 5: Function Table for A<B
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A<B
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A<B
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Notes: 5
The function table for the output A<B represents the output of the circuit logic line representing A<B for 16 combinations of the 2-bit numbers A and B.
The input numbers A and B are represented by A1A0 and B1B0 columns of the function table
Output A<B line is set to 1 when A<B.
Thus for input combinations of A and B that is 00 01, 00 10, 00 11, 01 10, 01 11 and 10 11 the output A<B is 1

## Slide 6: Karnaugh Map for A>B
A1A0/ B1B0 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 1 | 0 | 0 | 0
11 | 1 | 1 | 0 | 1
10 | 1 | 1 | 0 | 0
Notes: 6
Simplifying expression for A>B through a 4-variable K-map yields A1B1*+A0B1*B0*+A1A0B0*
Note that the left most column has binary values 00, 01, 11 and 10 representing A1A0
The top row has binary values 00, 01, 11 and 10 representing B1B0

## Slide 7: Karnaugh Map for A=B
A1A0/ B1B0 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 0 | 1 | 0 | 0
11 | 0 | 0 | 1 | 0
10 | 0 | 0 | 0 | 1
Notes: 7
Simplifying expression for A=B through a 4-variable K-map yields A1*A0*B1*B0*+A1*A0B1*B0+A1A0B1B0+A1A0*B1B0*

## Slide 8: Karnaugh Map for A<B
A1A0/ B1B0 | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 1
01 | 0 | 0 | 1 | 1
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 1 | 0
Notes: 8
Simplifying expression for A<B through a 4-variable K-map yields A1*B1+A1*A0*B0+A0*B1B0

## Slide 9: Quine-McCluskey Method
Difficult to manage K-maps of more than 4 variables
With a 4-variable K-map optimum groups of 1s and 0s are not formed

## Slide 10: Karnaugh Map
AB/ CD | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 1 | 0
Notes: 10
In the 4-variable K-map 6 groups of 4 cells each are formed.
The 6 groups form the six terms
AB, AC*, AD, BC, CD, B*D
Out of these six groups three groups are redundant and therefore they are introducing three extra product terms which are not required.
The essential terms that are required are AC*, BC and B*D

## Slide 11: Karnaugh Map
AB/ CD | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 0
01 | 0 | 1 | 1 | 1
11 | 1 | 1 | 1 | 0
10 | 0 | 0 | 1 | 0
Notes: 11
In the 4-variable K-map 5 groups of 4 cells and 2 cells are formed.
The 5 groups form the five terms
ABC*, ACD, A*BC, A*C*D and BD
Out of these five groups the largest group of 4 cells is redundant and therefore it is introducing an extra product term which is not required.
The essential terms that are required are ABC*, ACD, A*BC and A*C*D